## Slide 1: SOURCE CODING THEOREMS I & II

## Slide 2: Source coding
Definition
Conversion of the o/p of a discrete memoryless source(DMS) into a sequence of binary symbols (ie binary codeword).
Device that performs this conversion – source encoder.

## Slide 4
Objective
To minimize avg bit rate required for representation of the source by reducing the redundancy of the information source.
Terms related to Source coding process
Codeword length
Average codeword length ()
Code efficiency
Code redundancy

## Slide 5: Source Coding theorem I
Sk is the discrete memory less source output and the bk is the source encoder output which is represented by 0s and 1s.
The encoded sequence is easily decoded at the receiver.

## Slide 6
Consider the source has an alphabet with k different symbols and the kth symbol Sk occurs with the probability Pk, where k = 0, 1…k-1.
Sk is assigned with binary code word bk, by the encoder having length lk, is measured in bits.
The average code word length of the source encoder is defined as
=
represents the average number of bits per source symbol

## Slide 7
If Lmin=minimum possible value of , then coding efficiency is defined as
With , we will have
when approaches unity, the code is said to be efficient (source encoder is efficient when η=1).
For this, the value Lmin has to be determined.

## Slide 8
Given a discrete memory less source of entropy H(S), the average code-word length for any source encoding can bounded as .
In simple terms, the code word is always greater than or equal to the source code. Code word symbols are greater than or equal to the source code alphabets.

## Slide 9
Therefore with Lmin=H(S), the source encoder efficiency in terms of Entropy H(S) can be written as
η = H(S)/
This is known as noiseless coding theorem as it provides encoding which is error-free, also known as Shannon’s first theorem.

## Slide 10
Code redundancy
By increasing redundancy of encoding, we can make the prob of error approach 0.

## Slide 11: Source Coding theorem II
Let there be a discrete memory less source with entropy H(S).
It is always possible to find a q-ary prefix code such that the expected value of the length of the code words allocated to the sequences of L source symbols satisfies:
+

## Slide 12: Numericals

## Slide 13
Q1: An analog s/g is expressed by the following eqn. Calculate Nyquist rate for this s/g.

## Slide 15
Q2: Find Nyquist rate and Nyquist interval for the signal

## Slide 18
A delta modulator is tested with a 10 kHz sinusodial signal, 1 V peak to peak at input. The signal applied is sampled 10 times the nyquist rate, then what is the minimum step size required to prevent slope overload?

## Slide 19
fs=10 fn= 10×2fm=200 kHz
Δ fs ≥ 2πfm Am
Δ ≥ {2π×(10×103)×0.5 }/ 200 kHz Δ ≥0.157 Volts

## Slide 20
A delta modulated system is designed to operate 5 times the Nyquist rate for a signal with 3 kHz bandwidth. The quantization step size is 250 mV. Calculate the maximum amplitude of a 2 kHz input sinusoidal for which the delta modulator does not show slope overload.

## Slide 21
Max freq in s/g fm = 3KHz
Nyquist rate fN = 2fm = 6KHz
sampling freq fs= 5 fN
Δ fs ≥ 2πfm Am
Given Δ
fm =2KHz values
Find Am
Am

## Slide 22: Compute the step size for a delta modulator without slope overload if the input is 4cos 2π120t

## Slide 24: Find the minimum sampling frequency (fs)min required to avoid slope overload when x(t) = cos(2π800t) and Δ = 0.1?

## Slide 26
Input to the DM is m(t)=cos2πfmt. Step size is 0.628V. Sampling rate is 40,000 samples/sec. Find the frequency at which the slope overload distortion occurs?

## Slide 27
Δ fs < 2π𝐴mfm
0.628× 40000< 2π𝐴mfm
fm > 0.628× 40000/2π*1
fm > 4kHz