## Slide 1: MONOSTABLE MULTIVIBRATOR USING 555 TIMER

## Slide 4
Initially lets assume timer o/p = 0 (stable state)
So
Q1 will become ON
So VC = 0. V at pin 6 =0.
So o/p of UC = 0
When no trigger is given, trigger pin is connected to Vcc .
So o/p of LC = 0
S=R=0 ----- O/p of FF = previous state = 0(stable state)
Timer o/p =0

## Slide 5: When trigger is applied
Trigger s/g is applied such that o/p of pin 2 goes below 1/3 Vcc.
Hence o/p of LC =1
o/p of UC is still at 0
S=1, R=0 ---- Q=1. Timer o/p goes HIGH(unstable state)
Q1 is OFF.
C will charge thru R1 towards Vcc.
So once triggering happens, C starts charging towards supply V.

## Slide 6
After triggering action, V at pin 2 is again Vcc.
So now again o/p of LC becomes 0
During charging, whenever V at pin 6 > 2/3 Vcc , o/p of UC = 1
S=0, R=1 ------ Q=0. Timer o/p =0 (stable)
Q1 will become ON
So C will start discharging thru Q1.
So again o/p of both UC & LC =0. so timer o/p =previous state = 0(stable state)

## Slide 7
T = 1.1 R1C

## Slide 8
When trigger is applied, a pulse is obtained for a short duration.
Duration of pulse depends upon charging of the capacitor.
T = 1.1 R1C
In this way, by changing R1 and C, we can design a MMV and we can change the timing of the pulse.

## Slide 9: Applications of MMV
For generating timing delays.
(By changing R1 and C, we can design a MMV and we can change the timing of the pulse. )
For frequency division.
(If we are applying a periodic trigger s/g at pin 2)
Time duration of o/p pulse T shud be slightly more than that of triggering s/g t. (T > t).
In that case o/p s/g freq will be half than the trigger s/g freq.

## Slide 11
For pulse width modulation (PWM)
Till now we used only internal reference voltages.
If we apply a modulating s/g at control pin, it is possible to generate PW modulated o/p.
Here ref V will continuously change based on this modulating s/g.
Depending on that o/p PW will continuously change.

## Slide 13: DESIGN
Vc(t) = VF + (VI – VF)
To find T
VI = 0
VF = Vcc
Vc(t) = 2/3 Vcc
R’ = R1

## Slide 14
T = 1.1 R1C