## Slide 1: ASTABLE MULTIVIBRATOR USING 555 TIMER

## Slide 4
Case 1: V2=V6=0
Whenever the ckt is jz turned on, cap C will be fully uncharged.
ie V at pin 2 & 6 will be =0.
so upper comparator(UC) o/p = 0
Lower comparator(LC) o/p = 1
S=1 and R=0 ---------o/p Q=1------o/p of 555 timer = logic HIGH (1)
When Q=1, so transistor Q1 will be in OFF condition. So cap C starts charging thru R1 and R2.

## Slide 5: Case 1: V2=V6=0

## Slide 6
Gradually V at pin 2 & 6 will start increasing.
Case 2: 1/3 Vcc < V2=V6 < 2/3 Vcc
Whenever V at pin 2 > 1/3 Vcc, o/p of LC =0.
Let V at pin 6 < 2/3 Vcc, then o/p of UC = 0.
S=0 and R=0 ----o/p Q =1 (previous state). Timer o/p = High.

## Slide 7
Case 2: 1/3 Vcc < V2=V6 < 2/3 Vcc

## Slide 8: Case 3: Vc > 2/3 Vcc

## Slide 9
When o/p Q=0, so transistor Q1 will be in ON condition. So cap C starts discharging thru Q1.
Vc starts decreasing.
Case 4:
As soon as V goes jz < 2/3 Vcc, then o/p of UC = 0.
o/p of LC =0
S=0, R=0 --- Q=0 (previous)
o/p of timer = 0
Q1 still ON.

## Slide 10: Case 5: when Vc goes jz < 1/3 Vcc
o/p of LC =1
o/p of UC = 0
S=1, R=0 ---- Q=1 .
o/p of timer = logic High.
When o/p Q=1, so transistor Q1 will be in OFF condition. So cap C starts charging thru R1 & R2.

## Slide 11
In this way, cap is charging btw 1/3 Vcc and 2/3 Vcc.
Bcoz of this charging & discharging of cap, we will see a transition in the o/p V.
During charging process, whenever Vc > 2/3 Vcc, there is a transition in the o/p from logic high to logic low.
During discharging process, whenever Vc < 1/3 Vcc, there is a transition in the o/p from logic low to logic high.

## Slide 13
Time t1 – time for which o/p of timer remains HIGH
Time t2 – time for which o/p of timer remains LOW
t1 >t2
Time t1 - time taken by cap to charge from 1/3 Vcc to 2/3 Vcc
Time t2 - time taken by cap to discharge from 2/3 Vcc to 1/3 Vcc

## Slide 14
t1 >t2
Charging is thru R1 and R2
Discharging thru R2 only.
Duty cycle is always > 50%
For 50 % duty cycle(symm square wave), R1 shud be =0. But in this case, pin 7 is directly connected to Vcc and extra current will flow thru Q1 when it is ON. This may damage Q1 and hence the timer.

## Slide 16
During the charging of this capr, diode will be ON.
Fwd res of diode RD < R2. so C will charge thru R1 and D.
t1 = 0.693(R1+RD)C
During the discharging of this capr, diode will be OFF.
C will discharge thru R2.
t2 = 0.693R2C
If we adjz R1 value such that (R1+RD) =R2 , then duty cycle =50%

## Slide 17
Or if we assume diode is ideal, RD =0.
t1 = 0.693R1C
t2 = 0.693R2C
Duty cycle = R1 / (R1+R2)
If we take R1 = R2, then duty cycle =50%
If we take R1 > R2, then duty cycle >50%
If we take R1 < R2, then duty cycle <50%

## Slide 18: Design
Vc(t) = VF + (VI – VF)
To find t1
VI = 1/3 Vcc
VF = Vcc
Vc(t) = 2/3 Vcc
R’ = R1 + R2

## Slide 19
t1 = 0.693 (R1 + R2) C
To find t2
VI = 2/3 Vcc
VF = 0
Vc(t) = 1/3 Vcc
R’ = R2
t2 = 0.693 R2C

## Slide 20
Total time T = t1 + t2
T = 0.693 (R1 + 2R2) C
Frequency f =
Duty cycle = = =
Duty cycle =