## Slide 1: ACTIVE FILTERS

## Slide 2
An electric filter is often a freq selective ckt that passes a specified band of freqs & blocks or attenuates s/gs of freqs outside this band.
Filters :
Analog / digital
Passive / active
Audio (AF)/ radio (RF) freq

## Slide 3
1. Analog or digital filters:
Analog filters are designed to process analog signals, while digital filters process analog signals using digital technique.
2. Active or Passive:
Depending on the type of elements used in their construction, filter may be classified as passive or Active elements used in passive filters are R, L, C.
Elements used in active filters are transistor, or op-amp in addition to R and C.

## Slide 4: 3. Audio (AF)/ radio (RF) freq :
The type of elements used dictates the operating freq range of the filter.
Eg: RC filters are used for AF or low freq opr
LC or crystal filters are employed at RF or HF. Especially bcoz of their high Q values, crystals provide more stable opr at HFs.

## Slide 5: Active filters offer the following advantages over passive filters:
Gain and Frequency adjustment flexibility: Since the op-amp is capable of providing gain, the i/p signal is not attenuated as it is in a passive filter. [Active filter is easier to tune or adjust].
No loading problem: Because of the high input resistance and low o/p resistance of the op-amp, the active filter does not cause loading of the source or load.

## Slide 6
Cost: Active filters are more economical than passive filter. This is because of the variety of cheaper op-amps and the absence of inductors.

## Slide 7
The most commonly used filters are these:
1. Low pass Filters
2. High pass Filters
3. Band pass filters
4. Band –reject filters
5. All pass filters.

## Slide 8: Frequency response of the active filters:

## Slide 9: Each of these uses op amp as active element and R and C as passive elements.

## Slide 10
Low pass filters:
It has a constant gain from 0 Hz to a high cutoff frequency fH.
At fH the gain is down by 3db.
The frequency between 0 Hz and fH ---- pass band frequencies where as the range of frequencies those beyond fH, that are attenuated includes the stop band frequencies.
Butterworth, Chebyshev and Cauer filter are some of the most commonly used practical filters.
The key characteristics of the Butter worth filter are that it has a flat pass band as well as stop band. For this reason, it is sometimes called flat- flat filters.
Chebyshev filter -> has a ripple pass band & flat stop band.
Cauer Filter -> has a ripple pass band & ripple stop band. It gives best stop band response among the three.

## Slide 11
High pass filter:
High pass filter with a stop band 0 < f < f L
pass band f > f L
fL low cut off frequency
f operating frequency.
Band pass filter:
It has a pass band between 2 cut off frequencies fH and fL where fH > fL and 2 stop bands: 0<f< fL and f > fH between the band pass filter (equal to fH - fL).

## Slide 12
Band reject filter (Band stop or Band elimination) :
It performs exactly opposite to the band pass.
It has a band stop between 2 cut-off frequency fL and fH and 2 pass bands: 0 < f < fL and f > fH
fC center frequency.

## Slide 13: FIRST ORDER LOW PASS BUTTERWORTH FILTER

## Slide 14: FIRST ORDER LOW PASS BUTTERWORTH FILTER

## Slide 15
First order LPF that uses an RC n/w for filtering.
op-amp is used in the non inverting configuration.
Resistor R1 & RF determine the gain of the filter.
According to the V divider rule,
V across capr V1 = Vin
V1 =
Output Voltage v0= (1+RF/R1) V1

## Slide 16: Overall gain V0/Vin = (1+Rf/R1)/(1+j2πfRC)
V0/Vin gain of filter as a fn of freq
AF is pass band gain of the filter
f = freq of i/p s/g
fH = high cut off freq of the filter

## Slide 17
Transfer function
H(s) =
H(jω) =

## Slide 18
The gain magnitude and phase angle of the equation of the LPF can be obtained by converting eqn. into its equivalent polar form as follows.
| | =
Opr of LPF can be verified from gain magnitude eqn as follows:
At very low frequencies, f < fH
| | AF

## Slide 19
At f =fH, | |= 0.707 AF
At f > fH, | |< AF
LPF has a constant gain AF from 0 to fH.
At fH, gain is 0.707AF and after fH it decreases at a constant rate with an increase in freq.
When the frequency increases by tenfold (one decade), the volt gain is divided by 10.
The gain falls by 20 dB (=20log10) each time the frequency is increased by 10.

## Slide 20
Hence the rate at which the gain rolls off fH = 20 dB/decade or 6dB/octave (octave --- two fold increase in frequency).
The frequency f = fH is called the cut off frequency because the gain of the filter at this frequency is down by 3 dB (=20 log 0.707) from 0Hz.
cut off frequency ---- break freq, -3dB freq, corner freq.

## Slide 21: Steps in Filter design:
LPF can be designed by implementing following steps.
1. Choose a value of high cut off frequency fH.
2. Select a value of C 1μf.
3. Choose the value of R using the relation
fH=1/2πRC
4. Finally select values of R1 and RF dependent on the desired pass band gain AF using
AF =(1+RF/R1)

## Slide 22: Frequency scaling
Once a filter is designed and if we need to change cut off freq from fH to new freq fH’ .
This procedure is called freq scaling.
Multiply either R or C (not both) , by the ratio
Variable cap C is not commonly used.
So use std value of C and find R for desired cut off freq.
This is bcoz, for non std value of res, a pot.can be used

## Slide 23: NUMERICALS
a) Design a LPF with cut off freq of 1 KHZ with a pass band gain of 2.
b) Also plot the freq response of LPF.
Using the freq scaling technique, convert 1 KHz cut off freq of LPF (of above question) to a cut off freq of 1.6 KHz.

## Slide 27: SECOND ORDER LOW PASS BUTTERWORTH FILTER

## Slide 28: Second order LP Butterworth filter:

## Slide 29
A second order LPF having a gain 40dB/decade in stop band.
A First order LPF can be converted into a II order type simply by using an additional RC network.
The gain of the II order filter is set by R1 and RF, while the high cut off frequency fH is determined by R2, C2, R3 and C3.
fH =

## Slide 30: Analysis of the Filter Circuit:

## Slide 32: Substituting V1 in (2) and solving for VA, we get

## Slide 33: Now, for op-amp in noninverting configuration, V0 = AF VA where AF = 1+ RF/R1
VA = V0 / AF

## Slide 38
As the order of s in the gain expression is two, the filter is called Second Order Low Pass Butterworth Filter.
The standard form of Second Order Butterworth Filter Transfer Function of any second order system is
---- (7)

## Slide 39
where
ξ = damping of system
ωn = natural frequency of oscillations
Comparing (5) and (7), we can say that
In case of Second Order Low Pass Butterworth Filter, this frequency is nothing but the cut-off frequency, ωH

## Slide 41: Replacing s by jω, the transfer function can be written in the frequency domain and hence, finally, can be expressed in the polar form as,

## Slide 42: When R2 = R3 and C2 = C3 , ωH2 = 1/R2C2
Eqn 6 becomes ------ Vo/Vin =
Vo/Vin =
=
|| =

## Slide 43
For 2nd order Butterworth LP filter, damping factor .
|| =

## Slide 44
At the fH, the gain is 0.707 AF i,e. 3 dB down from its 0 Hz level.
After, fH ( f > fH ), the gain rolls off at a frequency rate of 40 dB/decade,.
Hence, the slope of the response after fH is – 40 dB/decade.

## Slide 45: Filter Design steps:
Except for having twice the roll off rate in the stop band, freq response of 2nd order LPF is identical to first order type.
Design steps are identical
1) Choose the cut-off frequency fH,
2) The design can be simplified by selecting R2 = R3 = R and C2 = C3 = C and choose a value of C 1 μF.
3) Calculate the value of R from the equation,

## Slide 46
4) As R2 = R3 = R and C2 = C3 = C, the pass band voltage gain AF = (1 + Rf/R1) of the second order LPF has to be equal to 1.586. AF =1.586
So RF = 0.586 R1
This gain is necessary to guarantee Butterworth response.
{ comparing eqns we have
2
0.707 , hence we get AF = 1.586 }

## Slide 47
Hence, choose a value of R1 ≤ 100 kΩ and calculate the corresponding value of RF.
The frequency scaling method for first order filter is equally applicable to the Second Order Low Pass Butterworth Filter.

## Slide 48: NUMERICALS
a) Design a 2nd order LPF with cut off freq of 1 KHZ.
b) Also plot the freq response of LPF.