## Slide 1: OP AMP WITH NEGATIVE FEEDBACK

## Slide 2: Introduction
Clipping occurs in open loop config when o/p attempts to exceed the saturation levels of op amp.
Since open loop gain of op amp is very high, only the smaller signals(µV or less)having very low freqs may be amplified accurately w/o distortion.
But this small s/gs are susceptible to noise.

## Slide 3
Besides being large, OL Voltage gain of op amp is not a constant. It varies with temp and power supply as well as mass production techniques.
Variations in V gain are relatively large in OL op amp. ------ unsuitable for many linear app.s
BW(band of freqs for which gain remains const) of most OL op amps is negligibly small. For this reason, the OL opamp is impractical in ac applctns.
Eg: OL BW of 741 IC is approx. 5 Hz. However, in almost all ac app.s , a BW larger than 5Hz is required.
For these reasons, OL op amp generally not used in linear apps.
Used for non linear cases like square wave generator.

## Slide 4: Feedback
We can select as well as control the gain of op amp if we use f/b.
o/p s/g is fed back to i/p either directly or via another network.
If the s/g fed back is of opp polarity or out of phase by 180 deg(or its odd integer multiple) w.r.to i/p s/g, f/b is called –ve f/b
An amplifier with –ve f/b has a self correcting ability against any change in o/p V caused by changes in environmental conditions.
-ve f/b also called as degenerative f/b because when used it degenerates(reduces) the o/p V amplitude and inturn reduces V gain.

## Slide 5
If s/g fed back is of same polarity or in phase with i/p s/g ……..+ve F/b
In +ve f/b, the f/b s/g aids the i/p. hence called as regenerative f/b.
Used in oscillator ckts.
When used in amplifiers, -ve f/b reduces V gain but advantages are :
  Stabilizes the gain
  Increases the BW
  Changes the i/p & o/p res.
  Decrease in harmonic or non linear distortion
  Reduction in the effect of variations in temp & supply V on the o/p of op amp

## Slide 7: Effect of negative feedback on amplifier performance:
The effect of negative feedback on an amplifier is considered in relation to gain, gain stability, distortion, noise, input/output impedance and bandwidth and gain-bandwidth product.

## Slide 8
Gain
Fig. shows a negative f/b ampr . A is the open loop gain of ampr, β is the f/b loop gain.
Here o/p of f/b ampr ------------ Vf=Voβ
Vo=AVi
Vo=A(Vs-Vf)
= A(Vs- Voβ)
Vo+A Voβ = AVs
Vo(1+A β) = AVs

## Slide 9
Overall gain or Closed loop gain
Af=
Af = ------------- for –ve f/b, gain decreases
Af = --------------for +ve f/b, gain increases

## Slide 10
Gain Stability:
An important advantage of negative voltage feedback is that the resultant gain of the amplifier can be made independent of transistor parameters or the supply voltage variations,
Af =
For negative voltage feedback in an amplifier to be effective, the designer deliberately makes the product Aβ much >> unity.
Therefore, in the above relation, ‘1’ can be neglected as compared to Aβ and the expression becomes
Af = A/(1+Aβ) = 1/β

## Slide 11
It can be seen that the gain now depends only upon feedback fraction, β, i.e., on the characteristics of feedback circuit.
As feedback circuit is usually a voltage divider (a resistive network), therefore, it is unaffected by changes in temperature, variations in transistor parameters and frequency.
Hence, the gain of the amplifier is extremely stable.

## Slide 12
Distortion:
A power amplifier will have non-linear distortion because of large signal variations.
The negative feedback reduces the nonlinear distortion.
Df= D/(1+Aβ)
Where D = distortion in amplifier without feedback
Df = distortion in amplifier with negative feedback
By applying negative feedback, the distortion is reduced by a factor (1+Aβ)

## Slide 13
Noise :
There are many no. of sources of noise in an amplifier.
The noise N can be reduced by the factor of (1+Aβ), in a similar manner to non-linear distortion, so that the noise with feedback is given by
Nf = N/(1+Aβ)

## Slide 14
Input / Output Impedance :
The input and output impedances will also improve by a factor of (1+Aβ), based on feedback connection type.

## Slide 15: Bandwidth and Gain-bandwidth Product:

## Slide 16
Each of higher and lower cut-off frequencies will improve by a factor of (1+Aβ). However, gain-bandwidth product remains constant.
BW of the amplifier:
This refers to the ‘band’ of frequencies for which the amplifier has a useful gain. Outside this useful band, the gain of the amplifier is considered to be insufficient compared with the gain at the centre of the bandwidth. The bandwidth specified for the voltage amplifiers is the range of freq.s for which the amplifiers gain is greater than 0.707 of the max. gain
decibels are used to indicate gain.

## Slide 17: Block diagram representation of f/b configurations
An op amp that uses a f/b ----- f/b amplifier.
Also called Closed loop amplifier bcoz f/b forms a closed loop(CL) btw i/p & o/p.
F/b ampr has 2 parts : an op amp & f/b ckt.
F/b ckt may be made up of either passive components, active comp or both.
In this, inorder to develop the basic f/b concepts, we are using only purely resistive f/b ckts.

## Slide 18
A CL ampr can be represented using 2 blocks: one for op amp and other for f/b ckt.
There are 4 ways to connect these 2 blocks.
These connections are classified acc to whether the Voltage or current is fed back to the i/p in series or parallel as follows:
Voltage series f/b
Voltage shunt f/b
Current series f/b
Current shunt f/b

## Slide 20
Voltage amplifier---Voltage series f/b --series-shunt feedback
voltage mixing and voltage sampling
Trans-resistance amplifier---Voltage shunt f/b---shunt-shunt feedback
Current mixing and voltage sampling
Trans-conductance ampr---Current series f/b------series-series feedback
Voltage mixing and current sampling
Current amplifier---Current shunt f/b---shunt-series feedback
Current mixing and current sampling

## Slide 21
In V series and V shunt, the V across load RL is the input voltage to the f/b ckt. The f/b quantity (either V or I) is the o/p of f/b ckt and is proportional to o/p Voltage.
In current series and current shunt, the load current IL flows into the f/b ckt. O/p of f/b ckt (either V or I) is proportional to the load current IL .
V series & V shunt ----most commonly used f/b.

## Slide 22: Voltage-Series Feedback
In this, a fraction of the output voltage is applied in series with the input voltage through the feedback circuit. This is also known as shunt-driven series-fed feedback, i.e., a parallel-series circuit.
The feedback circuit is placed in shunt with the output but in series with the input.

## Slide 23
As the feedback circuit is connected in shunt with the output, the output impedance is decreased and due to the series connection with the input, the input impedance is increased.

## Slide 24: Voltage-Shunt Feedback
In this, a fraction of the output voltage is applied in parallel with the input voltage through the feedback network. This is also known as shunt-driven shunt-fed feedback i.e., a parallel-parallel type.
The feedback circuit is placed in shunt with the output and also with the input.

## Slide 25
As the feedback circuit is connected in shunt with the output and the input as well, both the output impedance and the input impedance are decreased.

## Slide 26: Current-Series Feedback
In this, the load current is applied in series to the feedback circuit. This is also known as series-driven series-fed feedback i.e., a series-series circuit.
It is evident that the feedback circuit is placed in series with the output and also with the input.

## Slide 27
As the feedback circuit is connected in series with the output and the input as well, both the output impedance and the input impedance are increased.

## Slide 28: Current-Shunt Feedback
In this, load current is applied in series to the feedback circuit. This is also known as series-driven shunt-fed feedback i.e., a series-parallel circuit.
It is evident that the feedback circuit is placed in series with the output but in parallel with the input.

## Slide 29
As the feedback circuit is connected in series with the output, the output impedance is increased and due to the parallel connection with the input, the input impedance is decreased.

## Slide 31
Effect of negative f/b on i/p & o/p impedance
Input impedance for the connection is dependent on whether series/shunt f/b is used.
For series f/b, i/p impedance is increased
For shunt f/b, i/p impedance is decreased
Output impedance for the connection is dependent on whether voltage/current f/b is used.
For voltage f/b, o/p impedance is decreased
For current f/b, o/p impedance is increased

## Slide 34
Advantages of a negative feedback amplifier:
It has highly stabilized gain--- circuit stability
It has fewer harmonics distortion
It has less frequency distortion
Input-output impedances can be modified as desired
It has less amplitude distortion
Reduces Noise Level.
Improves Frequency Response & Bandwidth.
More Linear Operations.

## Slide 35
Disadvantages of a negative feedback amplifier:
Its reduction in gain
It increases output resistance in the case of current shunt and current series feedback amplifiers
It decreases input resistance in the case of voltage shunt and current shunt feedback amplifiers
Applications of –ve f/b
In almost all electronic components
In the regulated power supplies
In wideband amplifiers

## Slide 36: Op Amp circuits with voltage series feedback
Schematic diagram of V series f/b ampr (non inverting ampr with f/b)

## Slide 37
f/b ckt composed of 2 resistors R1 and RF
This is also called non inverting ampr with f/b or closed loop non inv ampr. Bcoz it uses f/b and the i/p is applied to non inv terminal i/p terminal of op amp.
OL V gain (gain w/o f/b) -------- A =
CL V gain (gain with f/b) -------- Af=
Gain of f/b ckt ------ β =
Vin ---- input voltage
Vf ------f/b voltage
Vid -----difference input Voltage

## Slide 38
Vid = Vin- Vf -----------------(1)
Feedback voltage always opposes the input voltage (or is out of phase by 180 deg wrto input voltage ) hence the feedback is negative.
Analysis of voltage series f/b ampr : performed by computing closed loop v gain, input & o/p resistances and BW.

## Slide 39: 1.CLOSED LOOP VOLTAGE GAIN (Af)
Af=
Vo=A(V1-V2)
From fig. V1=Vin
By Voltage division rule, ----- V2= Vf= Vo
Therefore
Vo=A(Vin- Vo )
Rearranging, we get ------------ Vo=

## Slide 40
Af= = (exact) ---------------(2)
generally A is very large . Typically
Therefore »
F ≈
Af= = = 1+ (ideal) ------------(3)
So by adjusting the values of resistor R1 & RF we can get the required gain .

## Slide 41
β = = -----------------(4)
comparing (3) & (4)
Af = (ideal) ---------(5)

## Slide 42
From eqn (2) Af= = (exact)
Rearranging eqn 2
Af=
Af = ----------------- (6)
Aβ is the loop gain

## Slide 43: Block diagram representation of non inverting ampr with f/b.

## Slide 44
OL V gain (gain w/o f/b) -------- A =
=
Ideal case: since A is very large , ≈ 0
That is v1 ≈ v2 (ideal)
V1 = Vin
V2=Vf = V0
So Vin= V0
Af= = = 1+ (ideal)

## Slide 45: 2. INPUT RESISTANCE WITH FEEDBACK
Equivalent ckt of a voltage series feedback ampr with the op amp

## Slide 46
Ri : open loop input res of op amp (w/o f/b)
RiF: closed loop input res of op amp (with f/b)
RiF = =
But vid =Vo / A and Vo= Vin
Therefore
RiF = Ri =ARi = ARi = Ri ()
RiF = Ri ()
Input res of op amp with f/b (V series f/b) is () times that w/o feedback.

## Slide 47: 3.OUTPUT RESISTANCE WITH FEEDBACK
Output res is the res determined looking back into feedback ampr from the o/p terminal as shown in fig.

## Slide 48
Res can be found by using Thevenin’s theorem for dependent sources.
To find o/p res with f/b RoF , reduce indep sources Vin to 0, apply an external voltage Vo and then calculate the resulting current
RoF =
Writing KCL at o/p node N,
Since [(Ri ││ R1)+ RF] >> Ro and as R0 is very small we have
Therefore
KVL at o/p loop
Vo- Ro -AVid = 0
=

## Slide 49
Vid = V1 –V2
We have V1=0 & V2=Vf
Vid = 0 –Vo = -βVo
Therefore = =
Substituting in RoF =
we get RoF =
Output res of V series f/b ampr is 1/ () times the o/p res Ro of op amp.
o/p res of op amp with –ve f/b is much smaller than o/p res w/o f/b.

## Slide 50: 4.BANDWIDTH WITH FEEDBACK
BW of an ampr is the range (band) of freqs for which the gain remains constant.
Manufacturers generally specify either gain BW pdt or supply open loop gain vs freq curve for the op amp.
For 741 op amp, the latter is typical.

## Slide 51: Open loop gain vs freq curve of the 741 IC

## Slide 52
From this fig, for a gain of 2* , the BW is approx. 5 Hz
GBW = 2 5 = 1MHz
On extreme end, BW =1 MHz, gain =1
GBW=1MHz * 1 = 1MHz
GBW is constant
This holds true only for op amps like 741 that have just 1 break freq below unity gain BW.
For 741, 5Hz is the break freq (fo). The freq at which gain A is 3dB down from its value at 0 Hz.
Freq at which gain equals 1 is called unity gain BW(UGB).
Since for an op amp with single break freq, GBW is constant and equal to UGB,

## Slide 53
UGB = A*fo
where A is OL voltage gain
fo is break freq of an op amp
Only for a single break freq op amp,
UGB = AF * fF
where AF is CL voltage gain
fF is bandwidth with feedback
Equating both eqns, we get
= AF * fF
fF =
For a non inv ampr, we have Af =

## Slide 54
Therefore fF = (1+Aβ)
BW of non inv ampr with negative feedback is (1+Aβ) times its BW w/o feedback.
fF =

## Slide 55: 5.TOTAL O/P OFFSET VOLATGE WITH FEEDBACK
In an op amp, when i/p is 0, o/p is also expected to be 0.
However bcoz of effect of i/p offset voltage and current, o/p is significantly large. This enhanced o/p voltage is called as total o/p offset voltage (VooT).
In an OL op amp, VooT is equal to either the +ve or –ve saturation voltage. Saturation voltages are specified in data sheet as o/p voltage swing.
Since with f/b, non inverting ampr gain changes from A to , VooT with f/b must also be times the voltage w/o feedback.

## Slide 56
Total o/p offset V with f/b =
VooT =
Where is always < 1 and ± Vsat = saturation voltages, max voltages the o/p of an op amp can reach.
In an OL configuration, even a very small voltage at the i/p of an op amp can cause the o/p to reach max value(+Vsat or –Vsat) bcoz of its very high V gain.
So from above eqn VooT can be either + or – voltage as Vsat can be either + or - .

## Slide 57
-ve f/b can also be used to reduce significantly the effect of noise variations in supply voltages and changes in temp on the o/p V of a non inv ampr.
Higher the value of (1+Aβ), the smaller is the effect of noise and variations in supply voltages and changes in temp on the o/p V of a non inv ampr.
From this analysis it is clear that non inv ampr with negative f/b exhibits the characteristics of perfect Voltage follower. That is it has very high i/p res, very low o/p res, stable V gain, large BW and very little (ideally 0) o/p offset voltage.

## Slide 58: Special case of non-inverting ampr with f/b
Voltage follower

## Slide 59: VOLTAGE FOLLOWER
Lowest gain that can be achieved from a non inv ampr with f/b is 1.
When the non inv ampr is configured for a unity gain, it is called as voltage follower bcoz o/p V is equal to and in phase with i/p.
o/p follows the i/p.
It is preferred bcoz it has higher i/p res and o/p amplitude is exactly = i/p.
To obtain V follower from non inv ampr with f/b, simply open R1 and short RF.

## Slide 60: Here all o/p V is fed back to the inv terminal of op amp. Consequently gain of f/b ckt is unity β = AF = 1
Fig : Voltage follower

## Slide 61
Since V follower is a special case of non inv ampr, the eqns are applicable as follows
β = AF = 1
RiF = A Ri since (1+A)≈A
RoF =
fF = A fo
VooT =
Voltage follower is also called as a non inverting buffer bcoz when placed btw 2 networks , it removes the loading on the first network.

## Slide 62: PROBLEMS

## Slide 63: Op Amp circuits with voltage shunt feedback
Fig: Voltage shunt f/b ampr using an op amp(or inverting ampr with f/b).

## Slide 64
The i/p voltage drives the inverting terminal
Amplified as well as inverted o/p signal is also applied to inv terminal via feedback res RF .
This arrangement forms a negative feedback bcoz any increase in the o/p signal results in a f/b signal into the inverting i/p causing a decrease in the o/p signal.
Non inv terminal is grounded and f/b ckt has only 1 res RF .
An extra res R1 is connected in series with i/p signal source Vin.

## Slide 65: 1.CLOSED LOOP VOLTAGE GAIN
KCL at i/p node V2
Since Ri is very large, the i/p bias current is negligibly small.
-----------(7)
Vo=A(V1-V2)
Since V1 =0 -------- Vo=-AV2
V2= - Vo /A

## Slide 66
Substituting V2 in (7)
AF = = (exact) ---------------(8)
-ve sign indicates that o/p and i/p are out of phase by 180 deg. Bcoz of this phase inversion, this config is called as inverting ampr with feedback.
since A is very lage (ideally ∞), >> F
So eqn (8) becomes AF = = (ideal) ----------(9)

## Slide 67
Divide both numerator and denominator of eqn (8) by (R1+RF)
AF = = = =
AF = -----------------(10)
K = voltage attenuation factor
= gain of f/b ckt
Comparing (6) & (10), in addition to phase inversion(-ve sign), CL gain of inverting ampr is K times the CL gain of non inverting ampr, where K<1

## Slide 68
Block diagram of inverting ampr with f/b using a voltage summing junction as a model for current summing
To derive the ideal CL gain, we can use (10) as follows
If Aβ>>1 -------- (1+Aβ)≈ Aβ
AF = = -------------(11)

## Slide 69: Inverting input terminal at virtual ground
Concept of virtual ground:
If any one of the input terminals of an op amp is grounded physically, the other i/p terminal will also be at ground potential, even though it is not grounded physically.
This is called as virtual ground concept in op amps.
i.e. differential i/p V in an op amp is ideally 0.
Vo = Avid Vid = Vo/A
Since A is very large (ideally infinite), Vid ≈ 0 and Vid= V1 – V2
That means V1 = V2 (ideal)
V at non inv i/p terminal of an op amp = V at inv i/p terminal of an op amp
(provided A is very large)

## Slide 70
So from the fig. of inv ampr with f/b
As V1 is at grnd --- V2 is approx. at grnd potential (by virtual grnd concept)
We have
-----------(7)
V1 = V2 = 0V
AF = = same result as in eqn (11)

## Slide 71: 2. INPUT RESISTANCE WITH FEEDBACK
Fig: Inverting ampr with Millerized feeback resistor.

## Slide 72: Miller theorem applied to op amp
The inverting op-amp configuration has a resistor connected from output to inverting input in Fig.(a)

## Slide 73
In Fig.(b), the inverting voltage amplifier has a gain of –A with input quantities of ν1 and I1 . The output voltage is νo . The equivalent input resistance can be found as follows. First, by definition of op-amp open-loop voltage gain, –A,
Vo=-AV1
At the i/p node apply KCL,
= I1
= (1+A) = I1
Eqvt input resistance
Rin = =

## Slide 74: For an amplifier with output resistance, the equivalent shunt contribution from RF is
Rout = =
Rout = = A Rin
The equivalent circuit resulting from Miller’s theorem is shown above in (b). The circuit has been converted by the Miller transform to an equivalent circuit that does not have an input-output bridging resistance.

## Slide 75: Easiest method of finding i/p res is to millerize the f/b res RF. Split RF into 2 miller components as shown in fig.

## Slide 76
Input res RiF = R1+ [ ││ Ri ] (exact) ---------(12)
Since Ri and A are very large, ││ Ri ≈ 0
Hence RiF = R1 (ideal) ---------(13)

## Slide 77: 3.OUTPUT RESISTANCE WITH FEEDBACK
ROF is the res measured at the o/p terminal of the f/b ampr.
Found using the Thevenin’s eqvt ckt. It is exactly same as that of non inv ampr bcoz o/p res of inv ampr must be identical to that of non inv ampr.
RoF = ----------(14)

## Slide 78: Fig: Thevenin’s eqvt ckt for RoF of the inverting ampr

## Slide 79: 4.BW WITH FEEDBACK
GBW pdt of a single break freq op amp is always constant.
Gain of ampr with f/b is always < gain w/o f/b.
Therefore BW of ampr with f/b (fF) must be > BW of ampr w/o f/b (fo)
fF = fo (1+Aβ) ------------ (15)
fo = break freq of op amp
= {true only for single break freq op amp such as 741}
Substituting this in eqn (15), we get
fF = (1+Aβ)

## Slide 80
fF = (1+Aβ)
fF = K ------------------(16)
Where K =
AF =
For the same CL gain, CL BW for inverting ampr is lower than that of non inv ampr by a factor of K (K<1)
When CL gain = 1 , BW will be
fF= UGB for non inv ampr &
fF = for inv ampr if R1 = RF

## Slide 81
As AF approaches A, the diff btw non inv and inv ampr BW approaches 0.
As an extreme limit, when K≈1, value of fF for both inv and non inv ampr is approx. same.

## Slide 82: 5.TOTAL OUTPUT OFFSET VOLTAGE WITH FEEDBACK
When the temperature & power supplies are fixed, o/p offset voltage is a function of gain of op amp.
We know that AF < A
Therefore VooT must always be smaller than that w/o f/b.
Total o/p offset V with f/b =
VooT =
± Vsat = saturation voltages

## Slide 83
Gain of f/b ckt β =
o/p V of op amp w/o f/b can be +Vsat or –Vsat bcoz of its very high V gain A.

## Slide 84: Special cases of inverting ampr with f/b
1. Current to voltage converter
2. Inverter.

## Slide 85: 1. CURRENT TO VOLTAGE CONVERTER
Ideal v gain of inverting amp
From eqn(9) ----------- AF = = (ideal)
Fig: current to voltage converter.

## Slide 86
Vo= RF
Since V1=0 and V1=V2
Vin/R1 = iin
= iin
Vo= - iin RF ------------ (17)
That is if we replace Vin and R1 by a current soure iin as shown in fig., o/p voltage Vo becomes proportional to i/p current iin.
that is, the ckt converts i/p current into a proportional o/p voltage.
Application : used in sensing current from photodetectors, in digital to analog converter applications.

## Slide 87: 2.INVERTER
If we need an output s/g equal in magnitude but opp in phase to that of i/p s/g, we use inverter.
The inverting amplifier ckt works as an inverter if R1 = RF .
All the eqns for inverting ampr are applicable here.
Here β = =
(1+Aβ) = (1+ )
The eqns can be applied by merely substituting () for (1+Aβ) since β=1/2.